CLEAN UP! COOL DOWN!
PC Cleaning and Maintenance
Ben Skidmore
November 2014

---
Why do we need to clean
inside our computers?
- They get full of dust and debris over time
- Dust causes heat buildup due to reduced airflow
- This leads to:
- Increased noise
- Shorter lifespan of components
- Increased risk of faults
IT IS IMPORTANT TO
CLEAN COMPUTERS PERIODICALLY

---
HOW AIR COOLING WORKS
- Biggest sources of heat need special cooling
- Heatsinks are attached to these components
- Airflow is created to move cool air around
- Warm air is ejected from the environment

---
Noise levels are improved for two reasons after cleaning:
- Fans run slower or switch off at lower temperatures
LESS FAN/MOTOR NOISE
- Fan blades are cleaner, creating less air turbulence when spinning
LESS AIRFLOW NOISE

---
KEY AIRFLOW POINTS
- Better airflow leads to better cooling ability
- Smooth, uninterrupted airflow leads to quieter operation
- Desktop PCs tend to have a more general airflow system
- Laptop PCs tend to have a very specific airflow system which is:
- More sensitive to dust and debris
- More prone to noise and overheating
LAPTOPS FAIL DUE TO HEAT-RELATED ISSUES
MUCH MORE FREQUENTLY THAN DESKTOPS

---
TYPICAL DESKTOP PC
LARGE FANS
SPACE FOR ADDITIONAL FAN
LOTS OF OPEN SPACE

---
TYPICAL LAPTOP
SMALL FAN
NO OPEN SPACE

---
THIS IS THE SINGLE EXHAUST POINT FOR THIS LAPTOP'S FAN!

---
What are the typical steps in a PC maintenance session?
Like a service for your car
1. Open the machine to access components
- Online guides are useful for laptops
2. Remove dust and foreign matter
- Dust on boards as well as cooling parts
3. Clean fan blade surfaces to improve their efficiency
- Fans can trap a lot of dust!
4. Consider changing thermal interface material (thermal paste)
- Thermal paste can dry out and become ineffective
5. Assess airflow and modify if necessary
- Desktops can be improved
- Laptops should be used on a flat surface!

---
BEST PRACTISE AND SAFETY
- Be aware of electrostatic discharge: Ground yourself
- Brushes and vacuum cleaners can generate ESD
- Exercise care while you work
- Be aware of electrical danger: switch off or unplug
- PPE: Dust can be very unpleasant

---
Which tools are needed for cleaning?
- SCREWDRIVERS
For opening cases or removing parts
- BRUSHES
Different sizes for dislodging stubborn dust
- CLOTH OR KITCHEN ROLL
More dust on a cloth means less in the air
- COMPRESSED AIR
For driving dust out of hard to reach areas gently
- VACUUM CLEANER
For removing majority of loose dust

---
Key heat sources in a typical computer:
CPU GPU CHIPSETS
Don't worry about technical details – LOOK FOR HEATSINKS OR FANS!

---
PLAN OF ACTION
1. Open case
- Discharge static!
2. Clear obvious buildup
- Remove parts trapping dust/debris
3. Dust/vacuum
- Avoid spinning fans!
- Take care with vacuum!
4. Assess airflow
- Cable routing
- Fan placement
5. Reassemble

---
(Thermal paste session)